## Slide 1: eMasters – Communication Systems E920 Wireless Communications
Notes, References, Questions, Problems, and Solutions
Venkateswar Reddy Melachervu
Jan 2023

## Slide 2: Lecture 1

## Slide 3: Key Concepts in Signal Processing
Power Signal
  A signal is said to be power signal if its average power is finite i.e.
  Total energy is
  Periodic signals are examples of power signals
  The average power of a signal is defined as the mean power dissipated by the signal such as voltage or current in a unit resistance over a period
Energy Signal
  A signal is said to be energy signal if and only if its total energy E is finite i.e.
  Average power 0
  Non-periodic signals are examples of energy signals
Taking the reference of electric circuits/signals
  The instantaneous power is
  Applying Ohm’s law ()
  When the value of resistance is 1, the power dissipated in it is known as normalized power
If is denoted by a continuous time signal
  The instantaneous power is equals to the square of the amplitude of the signal

## Slide 4: Key Concepts in Signal Processing
Power and energy - Continuous Time Case
  Average power or normalized power of continuous time signal is given by
  Total energy or normalized energy of a continuous time signal is defined as
    Joules
Power and energy - Discrete Time Case
  For the discrete time signal , the integrals above are replaced by summations
  Hence the total energy or normalized energy of is
  The average power or normalized power of is given by
Important Points
  Power and energy signals are mutually exclusive – no signal can be both power signal and energy signal
  A signal is neither energy nor power signal if both energy and power of the signal are equal to infinity
  All practical signals have finite energy; thus they are energy signals
  All finite duration and finite amplitude signals are energy signals
  Some of an energy signal and power signal is a power signal
  A signal whose amplitude is constant over infinite duration is a power signal
  The energy of a signal is not affected by the time shifting and time inversion. It is only affected by the time scaling

## Slide 5: Key Concepts in Signal Processing
Average power
  The average power of a signal is defined as the mean power dissipated by the signal such as voltage or current in a unit resistance over a period
Parseval’s Power Theorem
  The power of a signal is equal to the sum of square of the magnitudes of various harmonic components present in the discrete spectrum
Energy
  Energy of a continuous time signal is defined as the area under the curve of square of magnitude of that signal
  The energy signal exists only of the energy (E) of the signal is finite, i.e., only if 0 < E < ∞
Rayleigh’s Energy Theorem
  Energy of a function i.e. the integral of the square of magnitude of a function is equal to the integral of the square of magnitude of its Fourier transform

## Slide 6: Energy Spectral Density and Autocorrelation
Energy Spectral Density or Energy Density or Energy Density Spectrum - ψ(ω)
  Distribution of energy of a signal in the frequency domain
Autocorrelation
  Gives the measure of similarity between a signal and its time delayed version
  The autocorrelation function of an energy signal x(t) is given by
    is called the delayed parameter
Relationship between ESD and autocorrelation
  The autocorrelation function and the energy spectral density (ESD) function ψ(ω) form a Fourier transform pair

## Slide 7: Power Spectral Density and Autocorrelation
PSD or Power Density or Power Density Spectrum
  The distribution of average power of a signal in the frequency domain and denoted by
Autocorrelation
  Gives the measure of similarity between a signal and its time-delayed version
  The autocorrelation function of a power (or periodic) signal with any time period T is given by
    is called the delayed parameter
Relationship between PSD and autocorrelation function
  The power spectral density function and the autocorrelation function of a power signal form a Fourier transform

## Slide 8: Modern Communication Technologies and Systems
Cutting edge wireless technologies
  Multiple Antennae Systems
    Multiple Input and Multiple Output - MIMO Technology
  OFDM – Orthogonal Frequency Division Multiplexing
    Large bandwidth divided into several sub-bands and multiple uses sub-carriers
  CDMA
    Spreading code
Modern cellular and wifi systems built on cutting edge wireless technologies
  LTE
  5G – NR
  802.11 AC, 802.11 AX

## Slide 9: Principles and Models of Modern Wireless Systems

## Slide 10: Basic Digital Communication

## Slide 11: Modern Wireline Digital Communication System
Four components
  Received signal y
  Transmitted signal x
  Noise n
  Channel
Signal to Noise Power Ratio
Simple model of a communication system
  n – Additive noise
Signal power
  Defined as
  - power
  E is expectation operator

## Slide 12: Gaussian Random Variable and PDF
AWGN – Additive White Gaussian Noise
White Noise
  A flat power spectral density
  The signal contains equal power within a fixed bandwidth at any centre frequency
Gaussian Noise
  Noise PDF is Gaussian in nature – probability distribution/density function
  Gaussian variables/systems are represented by Gaussian PDF function
  Gaussian PDF
    Peak at the centre is mode
    Peak coincides with the mean (measure of centrality)
    Unimodal distribution
    Width/spread of PDF is variance
  Noise is represented by using Gaussian PDF equation
      Measure of Centrality
      Measure of spread
      Larger the spread, larger the noise power

## Slide 13: Additive Gaussian Noise
  Typically for noise
=

## Slide 14: Lecture 2

## Slide 15: White Noise
Noise PSD (Power Spectral Density) is flat across the entire frequency spectrum
Power distribution is uniform across all frequency components - Similar to white light
Contains all the frequency components

## Slide 16: Random Process Characterization - Power Spectral Density
Random process is a random variable at every instant of time
Power Spectral Density
  Measure of the signal’s power
  The power spectrum of a time series describes the distribution of power into frequency components composing that signal
  According to Fourier Analysis, any physical signal can be decomposed into a number of discrete frequencies or spectrum of frequencies over a continuous range
  The statistical average of a certain signal as analysed in terms of its frequency content is called Spectrum
  PSD refers to spectral energy distribution that would be found per unit time
  Summation or integration of the spectral components yields the total power for a physical processor or variance in a statistical process which is identical to what would be obtained by integrating over the time domain as per Parseval’s theorem (Rayleigh’s Energy Theorem or Rayleigh’s Identity)
One of the important tools to characterize random process is the power spectral density
For deterministic signal, Fourier transform provides the spectrum of the signal
For random process/signal, we determine the power spectral density which gives the distribution of power across different frequencies in the spectrum
Power spectral density of random process/variable is derived from auto-correlation function
PSD of a random process/signal is the Fourier transform of auto-correlation function

## Slide 17: Stationary Process
Strict/strong stationary process is a stochastic process whose unconditional joint probability distribution does not change when shifted in time
Consequently, parameters such as mean and variance also do not change over time
Definitions
  Joint probability
    Given two random variables that are defined in the same probability space, the joint probability distribution is the corresponding probability distribution on all possible pairs of outputs
  Probability space
    Also called a probability triplet comprising of
      Sample space of all possible outcomes -
      Event space set of events/outcomes in the sample space -
      Probability function Event probability in the event space – between 0 and 1
    Represented by {}
Strict sense stationarity
  Let be a stochastic process
  Let represent cumulative distribution function of the unconditional joint distribution of at times , ,
  Then is said to be strictly stationary or strict sense stationary if:
    for all and for all
    Since does not affect , is not a function of time

## Slide 18: PSD
PSD is a Fourier transform of auto-correlation

## Slide 19: Intro to MIMO System
Multiple-Input Multiple-Output Antenna System
Key technology used in
  4G LTE
  5G-NR
  WLAN – 802.11n, AC, AX
MIMO can lead to significant increase in data rates via parallel transmission – Same time and same bandwidth
  This phenomena – multiplexing several information streams in spatial domain is called – Spatial Multiplexing
MIMO system model
  r is the receive antennae and t is the transmit antennae
  It’ll be called as rxt MIMO system
  Mathematically represented as
is the channel coefficient between receive antenna and transmit antenna

## Slide 20: MIMO Receiver
Given , how to determine ?
“r” equations and “t” unknowns
  If H is non-singular (determinant 0, i.e. invertible i.e. exists), has a unique solution - is called estimated vector
What happens when r>t
  More equations – y (r) than unknowns – x (t) in H
  That means more rows than columns tall matrix H is not invertible no solution
  However, we try to find approximate solution
    Find such that is minimum
    min min - Least square norm error and called as Least Squares Problem
ZF - Zero Forcing Receiver
  is termed as pseudo-inverse of H – Tall matrix formula
    Because

## Slide 21: MIMO LMMSE Receiver
Linear Minimum Mean Square Error Receiver
  min
Covariance matrix of
Covariance matrix of
Cross-covariance matrix of
General expression of LMMSE receiver is
- rxr
Alternate LMMSE expression
  - txt
At high SNR ( - tens to be zero forcing receiver

## Slide 22: SVD
Singular value decomposition
Given , SVD is defined as
  U,V are ortho-normal matrices
  has the structure (rxt)
    and arranged in decreasing order and are singular values
    Singular values of any matrix are non-negative real number numbers whereas eigenvalues can be complex, negative, or positive
    Rank of H is number of non-zero singular values

## Slide 23: SVD Relation to Eigenvalue Decomposition
  are non-zero eigenvalues of
  V contains eigen vectors of
  are non-zero eigenvalues of
  U contains eigen vectors of

## Slide 24: SVD Processing

## Slide 25: Capacity of MIMO Wireless Systems

## Slide 26: Alamouti Code

## Slide 27: BER of Alamouti Code

## Slide 28: Multi-carrier Modulation

## Slide 29: OFDM

## Slide 30: OFDM System Model

## Slide 31: OFDM Examples

## Slide 32: BER Performance of OFDM Systems

## Slide 33: MIMO-OFDM

## Slide 34: ISI Channel Model

## Slide 35: Doppler Shift