## Slide 1: eMasters – Communication Systems E920 Wireless Communications
Notes, References, Questions, Problems, and Solutions
Venkateswar Reddy Melachervu
Jan 2023

## Slide 2: Key Concepts in Signal Processing
Power Signal
  A signal is said to be power signal if its average power is finite i.e.
  Total energy is
  Periodic signals are examples of power signals
  The average power of a signal is defined as the mean power dissipated by the signal such as voltage or current in a unit resistance over a period
Energy Signal
  A signal is said to be energy signal if and only if its total energy E is finite i.e.
  Average power 0
  Non-periodic signals are examples of energy signals
Taking the reference of electric circuits/signals
  The instantaneous power is
  Applying Ohm’s law ()
  When the value of resistance is 1, the power dissipated in it is known as normalized power
If is denoted by a continuous time signal
  The instantaneous power is equals to the square of the amplitude of the signal

## Slide 3: Key Concepts in Signal Processing
Power and energy - Continuous Time Case
  Average power or normalized power of continuous time signal is given by
  Total energy or normalized energy of a continuous time signal is defined as
    Joules
Power and energy - Discrete Time Case
  For the discrete time signal , the integrals above are replaced by summations
  Hence the total energy or normalized energy of is
  The average power or normalized power of is given by
Important Points
  Power and energy signals are mutually exclusive – no signal can be both power signal and energy signal
  A signal is neither energy nor power signal if both energy and power of the signal are equal to infinity
  All practical signals have finite energy; thus they are energy signals
  All finite duration and finite amplitude signals are energy signals
  Some of an energy signal and power signal is a power signal
  A signal whose amplitude is constant over infinite duration is a power signal
  The energy of a signal is not affected by the time shifting and time inversion. It is only affected by the time scaling

## Slide 4: Key Concepts in Signal Processing
Average power
  The average power of a signal is defined as the mean power dissipated by the signal such as voltage or current in a unit resistance over a period
Parseval’s Power Theorem
  The power of a signal is equal to the sum of square of the magnitudes of various harmonic components present in the discrete spectrum
Energy
  Energy of a continuous time signal is defined as the area under the curve of square of magnitude of that signal
  The energy signal exists only of the energy (E) of the signal is finite, i.e., only if 0 < E < ∞
Rayleigh’s Energy Theorem
  Energy of a function i.e. the integral of the square of magnitude of a function is equal to the integral of the square of magnitude of its Fourier transform

## Slide 5: Energy Spectral Density and Autocorrelation
Energy Spectral Density or Energy Density or Energy Density Spectrum - ψ(ω)
  Distribution of energy of a signal in the frequency domain
Autocorrelation
  Gives the measure of similarity between a signal and its time delayed version
  The autocorrelation function of an energy signal x(t) is given by
    is called the delayed parameter
Relationship between ESD and autocorrelation
  The autocorrelation function and the energy spectral density (ESD) function ψ(ω) form a Fourier transform pair

## Slide 6: Power Spectral Density and Autocorrelation
PSD or Power Density or Power Density Spectrum
  The distribution of average power of a signal in the frequency domain and denoted by
Autocorrelation
  Gives the measure of similarity between a signal and its time-delayed version
  The autocorrelation function of a power (or periodic) signal with any time period T is given by
    is called the delayed parameter
Relationship between PSD and autocorrelation function
  The power spectral density function and the autocorrelation function of a power signal form a Fourier transform

## Slide 7: Modern Communication Technologies and Systems
Cutting edge wireless technologies
  Multiple Antennae Systems
    Multiple Input and Multiple Output - MIMO Technology
  OFDM – Orthogonal Frequency Division Multiplexing
    Large bandwidth divided into several sub-bands and multiple uses sub-carriers
  CDMA
    Spreading code
Modern cellular and wifi systems built on cutting edge wireless technologies
  LTE
  5G – NR
  802.11 AC, 802.11 AX

## Slide 8: Principles and Models of Modern Wireless Systems
Large Scale Fading
  Due to path loss of signal as a function of distance and shadowing by large structures – buildings and hills
  Occurs as mobile moves through a distance of the order of the cell size
  Frequency independent
Small Scale Fading
  Due to constructive and destructive interference of the multiple signal paths between the transmitter and receiver
  Occurs at the spatial scale of the order of the carrier wavelength
  Frequency dependent

## Slide 9: Modern Communication Technologies and Systems
Cutting edge wireless technologies
  Multiple Antennae Systems
    Multiple Input and Multiple Output - MIMO Technology
  OFDM – Orthogonal Frequency Division Multiplexing
    Large bandwidth divided into several sub-bands and multiple uses sub-carriers
  CDMA
    Spreading code
Modern cellular and wifi systems built on cutting edge wireless technologies
  LTE
  5G – NR
  802.11 AC, 802.11 AX

## Slide 10: Modern Communication Technologies and Systems
Cutting edge wireless technologies
  Multiple Antennae Systems
    Multiple Input and Multiple Output - MIMO Technology
  OFDM – Orthogonal Frequency Division Multiplexing
    Large bandwidth divided into several sub-bands and multiple uses sub-carriers
  CDMA
    Spreading code
Modern cellular and wifi systems built on cutting edge wireless technologies
  LTE
  5G – NR
  802.11 AC, 802.11 AX

## Slide 11: Modern Wireline Digital Communication System
Channel is fixed
Signal to Noise Power Ratio
Simple model of wireline communication system
  Four components
    Received signal y
    Transmitted signal x
    Noise n
    Channel
  SNR – Signal to Noise Power Ratio
  Simplified model
    n – Additive noise
Signal Energy
  The energy of a continuous-time signal x(t) is defined as:
  The energy of a discrete-time signal x[n] is
  Physical interpretation
    Energy above does not refer to a specific physical property
    Instead, it describes the size of the signal
    The energy above, however, can be related to electrical energy
    If x(t) is the voltage signal across a load of resistance R, then the energy supplied to that load is

## Slide 12: Modern Wireline Digital Communication System
Signal Power or Average power
  The power of a continuous-time signal x(t)
    If the signal is periodic =>
  The power of discrete-time signal
    When the signal is periodic
      N is the period of periodic signal
  Physical interpretation
    Power above does not refer to a specific physical property
    Instead, it describes the size of the periodic signal
    The power above, however, can be related to electrical power
    If x(t) is the voltage signal across a load of resistance R, then the power supplied to that load is
  – Expected average value of power

## Slide 13: Additive White Gaussian Noise
Noise
  Most common model for noise is Gaussian - the noise samples follow the Gaussian density function
  In other words noise PDF is Gaussian in nature – probability distribution/density function
  Gaussian variables/systems are represented by the Gaussian PDF function
    Peak at the centre is the mode
    Peak coincides with the mean (a measure of centrality)
    Unimodal distribution
    Width/spread of PDF is the variance
  Typically, noise has a zero mean () value, then
    Noise PDF -
  In the context of zero mean noise, variance becomes power
      Measure of spread
      Larger the spread, larger the noise power
Where does

## Slide 14: Additive White Gaussian Noise
Where does
White noise
  To say that is a white noise means merely the successive samples are uncorrelated
  Where denotes the expected value random variables of
  In other words, the autocorrelation function of white noise is an impulse at lag 0
  Since power spectral density is the Fourier transform of the autocorrelation function, the PSD of white noise is constant
  Therefore white noise power spectral density is flat or constant across the frequency spectrum
  Power spectral density of white noise is given as
  Similar to white light – contains all frequency components
White Gaussian noise is additive in nature

## Slide 15: Random Process Characterization - Power Spectral Density
For deterministic signal
  a Fourier transform gives the spectrum of the signal (distribution of power across different frequencies in the spectrum)
For random process or signal
  Power spectral density gives the distribution of power across different frequencies in the spectrum
Random process is a random variable at every instant of time
One of the important tools to characterize random process is the power spectral density
Power Spectral Density
  Measure of the signal’s power
  The power spectrum of a time series describes the distribution of power into frequency components composing that signal
  According to Fourier Analysis, any physical signal can be decomposed into a number of discrete frequencies or spectrum of frequencies over a continuous range
  The statistical average of a certain signal as analysed in terms of its frequency content is called Spectrum
  PSD refers to the spectral energy distribution that is depicted per unit time
  Summation or integration of the spectral components yields the total power for a physical processor or variance in a statistical process which is identical to what would be obtained by integrating over the time domain as per Parseval’s theorem (Rayleigh’s Energy Theorem or Rayleigh’s Identity)
Power spectral density of a random process or variable is derived from the auto-correlation function
PSD of a random process or signal is the Fourier transform of auto-correlation function

## Slide 16: Stationary Process
Strict/strong stationary process is a stochastic process whose unconditional joint probability distribution does not change when shifted in time
Consequently, parameters such as mean and variance also do not change over time
Definitions
  Joint probability
    Given two random variables that are defined in the same probability space, the joint probability distribution is the corresponding probability distribution on all possible pairs of outputs
  Probability space
    Also called a probability triplet comprising of
      Sample space of all possible outcomes -
      Event space set of events/outcomes in the sample space -
      Probability function Event probability in the event space – between 0 and 1
    Represented by {}
Strict sense stationarity
  Let be a stochastic process
  Let represent cumulative distribution function of the unconditional joint distribution of at times , ,
  Then is said to be strictly stationary or strict sense stationary if:
    for all and for all
    Since does not affect , is not a function of time

## Slide 17: Auto-correlation, Cross Correlation and Power Spectral Density
Correlation
  If X,Y are two complex-valued random variables, the correlation between these two random variables is defined as
  A higher correlation between X,Y indicate a higher degree of similarity between the values assumed by these random variables
  Degree/strength of the correlation can be measured by correlation coefficient
  A positive correlation coefficient
    As one variable increases, the other variable also tends to increase
  A negative correlation coefficient
    As one variable increases, the other variable tends decreases
  Zero correlation coefficient
    No relationship between the variables
Auto-correlation or serial correlation
  Degree to which a time series is correlated with itself over time
  Measure of how the values of a variable at different time points are related to each other
  Autocorrelation is commonly used in time series analysis to detect patterns and trends in data
Cross Correlation
  Degree of similarity between two time series or between two signals at different lags or time intervals
Power spectral density
  PSD is calculated using the Fourier transform of a signal or time series
  PSD is usually plotted with frequency on x-axis and power or energy on y-axis

## Slide 18: PSD of Random Process and White Noise
One of the important tools to characterize a random process is the power spectral density
PSD of a random process depicts the distribution of power/energy across different frequencies in the spectrum
PSD of a random process is derived from the auto-correlation function
Auto-correlation of Random Process
  Two samples of noise at time k is and time (n+l) is a lag of l from k
  The correlation between these two samples i.e. the expected value of
  If the correlation depends only on lag l and does not depend on the time instant k, such a random process is known as Wide Sense Stationary Random Process
White Gaussian Noise
  Typically the white noise is a wide sense stationary random process
  Particularly for white noise, the auto-correlation is simply an impulse -
  Any two samples of white noise are un-correlated and coupled with the fact these are Gaussian which means these are independent noise samples- IID – independent identically distributed samples
  When we take the Fourier transform of white noise auto-correlation function we get the PSD
  The PSD of white noise i.e. Fourier transform of an impulse is flat across entire frequency spectrum -

## Slide 19: Notes – Power of a Signal and PSD of White Noise
Power of a signal
  Measure of the amount of energy in the signal
  Commonly computed as mean squared value of the signal over a given interval
  The power P of continuous signa x(t) over the interval [t1, t2]
  The power of a signal is closely related to its variance which is how much the signal values deviate from their mean value
  The variance of a continuous signal x(t) over an interval [t1,t2] is defined as
  Why the power of a signal is equal to its variance, let’s use the following property of variance
    If the signal x(t) has zero mean i.e. , then
  In other words, the variance of a zero mean signal is equal to the expected value of the signal’s magnitude squared
  For a signal with non-zero mean, the power can be obtained by subtracting the mean value of the signal before computing the mean squared value

## Slide 20: Wireline SNR – Signal to Noise Power Ratio
~ - P is the power of the signal
Approximately constant because channel is fixed
Hence no variations or fluctuations in SNR and hence performance is fixed

## Slide 21: Performance of Communication System
BER is the probability that a single received bit is in error
Bit Error Rate is an important metric for communication system performance

## Slide 22: Digital Modulation - BPSK
Mapping of information bits to signals that can be transmitted over the channel
There are various formats for digital modulation
  BPSK, QPSK, QAM
BPSK – Binary Phase Shift Keying
  Two Phases - are employed to indicate the information
  Signal Constellation : - 2 points/symbols
  A is amplitude-voltage
  If there M points/symbols in the constellation, the number of bits per symbol will be
  Number of bits per symbol in BPSK -
  Consider signal power P
  Expected value -
Communication system model for BPSK

## Slide 23: BPSK Wireline Performance
Signal power – P
Noise power -
SNR is
BER for BPSK over wireline channel
Standard Gaussian RV
  PDF -
Gaussian Q function
  Relates to PDF and is CCDF – complementary cumulative distribution function of the standard Gaussian RV
    CDF -
    CCDF -
    We can obtain PDF from CDF
      PDF -
Q Function Q(x) - CCDF

## Slide 24: QPSK
Quadrature Phase Shift Keying
  Quadrature -
Quadrature Carrier Multiplexing
  Cos and Sine waves - to each other – Orthogonal
Constellation is given as
    Above two are orthogonal carriers
  Any communication signal can be expressed as a combination of two signals
  2 times the rate bandwidth
  QPSK constellation
  QPSK bits per symbol =
  If the power is P
  Phases of the symbols are -
  Phase differences between any successive points/symbols are

## Slide 25: QPSK
Mapping of the Symbols can be:
Communication system model
  - 𝑎𝑟𝑒 𝑐𝑜𝑚𝑝𝑙𝑒𝑥 𝑏𝑎𝑠𝑒𝑏𝑎𝑛𝑑 𝑟𝑒𝑝𝑟𝑒𝑠𝑒𝑛𝑡𝑎𝑡𝑖𝑜𝑛𝑠 𝑜𝑓 𝑟𝑒𝑐𝑒𝑖𝑣𝑒𝑑 𝑠𝑖𝑔𝑛𝑎𝑙, 𝑡𝑟𝑎𝑛𝑠𝑚𝑖𝑡𝑡𝑒𝑑 𝑠𝑖𝑔𝑛𝑎𝑙, 𝑛𝑜𝑖𝑠𝑒, 𝑟𝑒𝑠𝑝𝑒𝑐𝑡𝑖𝑣𝑒𝑙𝑦 and are complex quantities
Signal power P
  For power
  In phase and quadrature components each will have half the power => P/2
  Signal amplitude A depends on the power and cannot be chosen arbitrarily
Noise power
  Noise will have real and complex parts each of which will have a power of and hence total noise power will be
  are Gaussian with
SNR for this system is
QPSK can be represented as two parallel streams of BPSK
BER of each BPSK stream (In phase or quadrature) is

## Slide 26: QPSK
QPSK symbol is in error when either of the bits (in phase and quadrature) is in error
Symbol Error Rate of QPSK

## Slide 27: QAM – Quadrature Amplitude Modulation
HOM – Higher Order Modulation
Most important constellations
Used in 4G,LTE, 5G-NR etc.
Generalization of QPSK
  QPSK is 4 QAM
Also called as
QAM is known as M-QAM – M is the number of symbols
QCM – Quadrature Carrier Multiplexing
Number of bits per symbols -
Square constellation
16 QAM
  A is amplitude and depends on the power and cannot be chosen arbitrarily
QAM allows to transmit at very high bit rates
  1024 QAM has

## Slide 28: QAM
AMC – Adaptive modulation and coding – is employed by mobile communication systems for effective communication
Symbol Error Rate for m-ary QAM is:
  SER

## Slide 29: Wireless Channel and Performance
Multiple propagation paths – LOS, and several NLOS – multipath propagation due to scatterers
Multipaths exists due to large objects or scatters
Multipath propagation leads to multiple copies of the signal at the receiver
Multiple signal copies causes superposition of the signals at the receiver resulting interference – constructive and destructive
Because of interference, the SNR varies or fluctuates
Due to interference, received signal power fluctuates or varies and this phenomenon is called fading
Wireless channel is also called fading channel - where the received power dips significantly is termed as deep fade

## Slide 30: Wireless Channel Model
Wireline channel model
Wireless channel model
  h fading channel coefficient and is complex quantity
  h has multiplicative effect on the signal
  h is represented as
    - In phase and quadrature entities
    Alternatively as
  h determines the output power – large if |h| is large, small if |h| is small
Fading channel coefficient
  Random in nature and modelled as
  real part and is imaginary part and and are independent Gaussian RVs
  Their mean is zero i.e. and variance is i.e.
  h is a symmetric complex Gaussian RV
  Mean - and Variance -
  h is a complex Gaussian variable with mean zero and variance unity – unit variance complex Gaussian
  Polar form of h is :

## Slide 31: Fading Channel Coefficient
Amplitude
  The channel coefficient h in the polar form is
  The amplitude a follows the Rayleigh PDF
  Rayleigh fading channel
Phase
  phase is uniformly distributed across
  PDF of phase =

## Slide 32: Symbol Detection – Equalization and Estimation
Channel estimation
  Technique used for determining the value of h to be accounted for at the receiver
  Performed by measuring the transmitted pilot stream of symbols – sequence of known symbols – at the receiver
Equalization
  Account or cancel or invert the effect of the channel coefficient h is known as equalization
  Dividing the received signal by a channel coefficient – a single number – is called as Single Tap Equalizer
It’s not always possible to simply divide by a coefficient to recover the original signal – especially when there is Inter-Symbol-Interference
Equalization process
  Example :
  Simple signal detection (z) at the receiver can be carried out as follows:
    This is termed as a Threshold Detector and threshold is zero
Mathematically rigorous framework that can guarantee signal detection is Maximum Likelihood (ML) Detector

## Slide 33: Wireless Channel Output SNR
Wireless system
The output power of the channel is =
  a is amplitude and real value whereas h is complex quantity
The channel output SNR, represented as is

## Slide 34: Wireless Channel Performance - BER
Instantaneous BER of BPSK =
  - The output SNR of the wireless channel
Instantaneous BER depends on amplitude a (|h|) which is a random quantity – Rayleigh random variable
Hence BER is an average with respect to the PDF of a which is follows Rayleigh PDF from the channel model of Rayleigh Fading channel -
The average of a function whose PDF is is
  The lower limit is actually zero
BER of Wireless BPSK
BER of Wireless QPSK

## Slide 35: BER of Rayleigh Fading Channel
Wireline
  The Q function – CCDF - the tail probability of Gaussian RV, x is
  The Q function can be approximately upper bounded by
  Wireline BER decreases exponentially with increase in SNR
Wireless
    At higher SNR, will be very small
    Applying Taylor series , where x is very small is first order Taylor series approximation
  Applying first order Taylor series approximation to BER
  Wireless BER only decreases as
The wireless channel requires an order of times more transmit signal power to maintain the same BER
This is due to deep fade or wireless channel being deep fading channel

## Slide 36: Deep Fade
For deep fade
Probability of Deep Fade
  As per Taylor series,
  When x is small,
  Simplifying further,
BER is highly correlated with deep fade

## Slide 37: BER and SER of QPSK and QAM
QPSK
  SNR of BPSK
  SNR of QPSK (2 BPKS streams)
  BER of each BPSK stream is
  Overall SER -
SER of M-ary QAM
Thus BER and SER are proportional to
Thus the wireless channel performance cannot be increased simply by changing the modulation
The solution to improve the wireless performance is diversity – multiple antennae

## Slide 38: Multiple Antennas and Diversity
Diversity is achieved through multiple links between transmitter and receiver
One simple technique for diversity is to use multiple antennas

## Slide 39: Intro to MIMO System
Multiple-Input Multiple-Output Antenna System
Key technology used in
  4G LTE
  5G-NR
  WLAN – 802.11n, AC, AX
MIMO can lead to significant increase in data rates via parallel transmission – Same time and same bandwidth
  This phenomena – multiplexing several information streams in spatial domain is called – Spatial Multiplexing
MIMO system model
  r is the receive antennae and t is the transmit antennae
  It’ll be called as rxt MIMO system
  Mathematically represented as
is the channel coefficient between receive antenna and transmit antenna

## Slide 40: MIMO Receiver
Given , how to determine ?
“r” equations and “t” unknowns
  If H is non-singular (determinant 0, i.e. invertible i.e. exists), has a unique solution - is called estimated vector
What happens when r>t
  More equations – y (r) than unknowns – x (t) in H
  That means more rows than columns tall matrix H is not invertible no solution
  However, we try to find approximate solution
    Find such that is minimum
    min min - Least square norm error and called as Least Squares Problem
ZF - Zero Forcing Receiver
  is termed as pseudo-inverse of H – Tall matrix formula
    Because

## Slide 41: MIMO LMMSE Receiver
Linear Minimum Mean Square Error Receiver
  min
Covariance matrix of
Covariance matrix of
Cross-covariance matrix of
General expression of LMMSE receiver is
- rxr
Alternate LMMSE expression
  - txt
At high SNR ( - tens to be zero forcing receiver

## Slide 42: SVD – Singular Value Decomposition
Mathematical technique for decomposing a matrix into 3 components
  A left singular matrix
  A diagonal singular values matrix
  A right singular matrix
Represented by
Provides a way to analyze the properties of a matrix – rank, eigenvalues, eigenvectors, singular values etc. which are related to the matrix norm and condition number
Used for decomposing the channel between transmitter and receiver into set of parallel sub-channels, each having different gains and phases
Used to find the optimal beamforming vectors that maximize the SNR for each sub-channel – a technique known as Singular Value Beamforming
Also used for transmit diversity – usage of multiple antennas at the transmitter to improve the reliability of transmission
By decomposing the channel matrix using SVD
  A transmitter can send different signals on each of the sub-channels with different powers based on their corresponding singular values
  This technique is known as STBC – Space-time Block Coding
  STBC improves the error performance of wireless systems

## Slide 43: SVD
Given , SVD is defined as
  U,V are ortho-normal matrices
  has the structure (rxt)
    and arranged in decreasing order and are singular values
    Singular values of any matrix are non-negative real number numbers whereas eigenvalues can be complex, negative, or positive
    Rank of H is number of non-zero singular values

## Slide 44: SVD Relation to Eigenvalue Decomposition
  are non-zero eigenvalues of
  V contains eigen vectors of
  are non-zero eigenvalues of
  U contains eigen vectors of

## Slide 45: SVD Processing

## Slide 46: Capacity of MIMO Wireless Systems

## Slide 47: Alamouti Code
The main idea behind Alamouti coding is to transmit the same data over multiple antennas in a way that maximizes diversity and protects against error – error protection coding
  If one of the antennas experiences fading or interference, the data can still be recovered from the other antenna
This is achieved by transmitting the data in a space-time block code, where the data is transmitted over multiple time slots and multiple antennas improving the reliability and capacity of transmission
Particularly useful when the transmitted signal is subjected to fading due to multipath propagation
It is a 2x1 Orthogonal STBC – used for 2 transmit antennae and 1 receive antenna system (a 1x2 (rxt) diverse system – MISO system)
It encodes two complex symbols onto two transmit antennae and transmits over two consecutive time slots providing diversity and improved SNR at the receiver
  In the first time slot, the two complex symbols are transmitted on the two antennas
  In the second time slot, the same two symbols are transmitted again, but with the conjugate of one symbol transmitted on the second antenna
Achieves diversity order 2 without the knowledge of the channel state information (CSI)for beamforming (channel coefficients being sent by the receiver) at the transmitter

## Slide 48: Alamouti Code
MISO channel is represented by
The first transmit vector is
The second transmit vector is
Hence
Hence output system of equations

## Slide 49: Alamouti Code
Columns of channel matrix of Alamouti system are orthogonal vectors
Hence Alamouti code is known as Orthogonal Space-time Block Code – OSTBC
Can be extended to arbitrary number of receive antennae
Since the matrix is orthogonal, decoding can be simply performed by multiplying by inverse
Inverse of Alamouti Matrix -
Decoder o/p =
Alamouti code transmits two symbols per two time instants with a net of one symbol per a time instant i.e. R=1 – such a code is termed a full rate code

## Slide 50: SNR and BER of Alamouti Code
SNR
  The available power P at the transmitter is split equally across two transmit streams/antennae
  Channel output SNR of each stream is -
    Where for BPSK and QPSK
  Alternatively,
BER
  The output BER of Alamouti Scheme for BPSK and QPSK

## Slide 51: OFDM Technology

## Slide 52: Single and Multi-carrier Modulation
Single Carrier System
  For a bandwidth B/2, the symbol time is
    Example : For a single carrier system of 10 MHz bandwidth, the symbol time is
  As the bandwidth increases, symbol time decreases or shrinks
  Due to multi-path in wireless channel, different copies of the transmitted signal arrive with different delays -
  As a result, multi-path components are spread over time which is called as Delay Spread
  For large bandwidth
    Delay Spread >> Symbol Time/Duration
  At higher bandwidths, the multi-path signal copies with different delays superimpose at the receiver causing ISI – Inter-symbol Interference increasing BER
How to eliminate ISI?
ISI can be eliminated using Multi-carrier Modulation (MCM) using OFDM

## Slide 53: What is OFDM
OFDM is widely employed in most of the modern cellular and wifi systems
MIMO-OFDM is one of the most widely used technologies today
  4G LTE, 5G-NR
  802.11n, 802.11ac, 802.11ax
Due its transmission over very large bandwidth, it enables ultra-high data rates
OFDM exploits frequency dimension and MIMO exploits space dimension
  Space + Frequency Multiplexing => Extra-ordinarily high data rates

## Slide 54: OFDM - Multi-carrier Modulation
Instead of using one carrier, use N carriers/sub-carriers
Divides the bandwidth into N sub-bands/carriers
Each sub-band bandwidth is across N bands, B is total bandwidth
The sub-carrier bandwidth is also called as sub-carrier spacing, sub-carrier bandwidth etc. –
Sub-carriers are placed at
If is called as placement is
As per signals and systems, the mathematical representation of a generic carrier of frequency is
sub-carrier is placed at and can be represented as
Modulate each sub-carrier with a symbol – Modulate sub-carrier with the symbol -
Hence the aggregate transmit signal becomes the sum of all modulated sub-carrier signals
  Also termed as symbol loaded on sub-carrier

## Slide 55: Fourier Series
Fourier series exists for a continuous periodic signal
For continuous periodic signals, Fourier series or complex exponential Fourier series or trigonometric Fourier series will be used
For continuous aperiodic signals, Fourier transform is used
For discrete aperiodic signals, Discrete-Time Fourier transform is used
For discrete periodic signals, Discrete Fourier Series is used
For discrete limited signals, FFT or DFT is used

## Slide 56: OFDM - Demodulation
Considering a noiseless and non-fading channel/scenario
is a Fourier series or complex exponential Fourier series of corresponding to fundamental frequency and various representing the Fourier coefficients
All frequencies are multiples of the fundamental frequency
Therefore to extract the which is a Fourier coefficient corresponding to the frequency , Fourier series procedure needs to be followed
The limits can be
is the OFDM symbol duration Delay Spread
Thus OFDM eliminates ISI

## Slide 57: OFDM - Demodulation
Extracting symbol
Coherent demodulation
Rewriting the above equation:
Sub-carriers are orthogonal
i.e. the sub-carrier orthogonality can leveraged to extract the symbol inner product between two sub-carriers that are orthogonal is zero
In summary
  Orthogonal – sub-carriers are orthogonal
  Frequency Division – Dividing bandwidth into multiple sub-carriers
  Multiplexing – Parallel transmission of multiple symbols over multiple sub-carriers in the same band – Wide Bandwidth Channel
  Enables transmission over large bandwidth without ISI – extremely high data rates

## Slide 58: OFDM Generation – IDFT IFFT
OFDM comprises of 1000s of sub-carriers difficult to generate!
Is there a simple technique to generate OFDM?
Yes – using sampling!
Considering signal BW is limited to , the sampling frequency is (Nyquist Criterion)
Sampling duration
The sample will be at
Scaling by factor
The expression is representation of IDFT – Inverse Discrete Fourier Transform
IDFT can be efficiently implemented using IFFT – Inverse Fast Fourier Transform
IFFT algo is widely implemented in DSP chipsets – computational complexity is
Tx
IFFT
Load/Modulate
Rx
Demodulation
Loaded Sub-carriers
IDFT
IFFT
Time domain samples
Sampling - 1/B

## Slide 59: ISI Channel Model
Fading channel model for a symbol ,
ISI channel model with interference from other/previous symbols in the band, for symbol
  Simplifying
    are called channel taps – channel filters
  y(k) can be further simplified as
  So, channel performs linear convolution

## Slide 60: Convolution
Convolution is a mathematical operation on two functions (f and g) that produce a third function (f*g) that expresses how the shape of one is modified by the other
The term convolution refers to both the resultant function and the process of computing it
The resultant function is defined as the integral of the product of the two functions after one is reflected on y-axis and shifted
Some features of convolution are similar to cross-correlation

## Slide 61: Cyclic Prefix – CP and Demodulation
The cyclic prefix are samples from the tail of OFDM generated by IFFT
Prior to transmission, the above cyclic prefix is prefixed to the IFFT output forming OFDM block
So the total number of samples in OFDM block are ,
is usually a maximum of 25%*N
What is the effect of CP?
Because of the addition of CP as prefix to the output of IFFT of OFDM, the linear convolution becomes circular convolution
The output of OFDM channel is
The output of the sub-carrier k -
When an FFT is taken for a circular convoluted time domain signal, it becomes the product between corresponding coefficients

## Slide 62: OFDM System Model
=0,1,2,…N-1 – sub-carriers
The OFDM System Model is
  …
Channel coefficient are given as
CP removal
  OFDM block =
  The prefixed CP is removed by the receive and receiver processes the output from
  This process is known as CP removal
What is OFDM achieving?
  Converting a time-domain ISI channel into N parallel ISI-free (flat fading) sub-carrier channels!
    ISI – Frequency selective, dispersive channel
    Flat fading – Frequency flat channel, ISI free

## Slide 63: OFDM Examples
The expressions and can be simplified using Euler’s formula
    = - Since cosine is even function
    = - Since sine is odd function

## Slide 64: BER Performance of OFDM Systems
Consider channel taps -
Assume they are Rayleigh fading with unit power
Noise samples are i.i.d with power
Symbols loaded on sub-carriers have power P
Effective SNR for QPSK as
    L – number of channel taps
    N – number of sub-carriers
BER of OFDM for QPSK

## Slide 65: MIMO-OFDM
Exploits spatial multiplexing of MIMO and frequency multiplexing of OFDM leading to ultra-high data rates
MIMO-OFDM channel model
  – number receive antennas
  – number of transmit antennas
  Channel taps between receive antenna i and transmit antenna j
  Total number of taps are
Transmission
  On each transmit antenna load the sub-carriers as below – i.e. perform IFFT
    – Frequency domain samples
  Total number of symbols =
  IFFT can be performed as shown below
    – time domain samples on transmit antenna
  One IFFT per each transmit antenna – total IFFT blocks at the transmitter
  Add CP on each transmit antenna
  What is the size of total transmission block – one OFDM block?
Channel
  Because of addition of CP, the linear convolution becomes circular convolution
Receiver
  FFT is performed at each receive antenna after removing CP
  is output on sub-carrier
  One FFT at each receive antenna FFTs

## Slide 66: Net MIMO-OFDM System Model
– vector of outputs for all Rx antennas on sub-carrier – output symbol vector
- MIMO channel matrix for sub-carrier – Channel matrix
- vector of symbols loaded on sub-carrier for all Tx antennas – transmit symbol vector
- Noise vector for sub-carrier – noise vector

## Slide 67: MIMO-OFDM Channel Coefficients
MIMO channel coefficients in the frequency domain corresponding to sub-carrier between receive antenna and transmit antenna
are given by the FFT of the channel taps and are frequency domain coefficients
  There are
Converted a frequency selective MIMO channel to a flat fading MIMO channel using OFDM

## Slide 68: MIMO-OFDM
MIMO-OFDM model for sub-carrier is
How many such parallel MIMO systems are there?
  One for each sub-carrier  N parallel MIMO channels
  ….
How to recover
  Any MIMO receiver – ZF or LMMSE receiver
ZF receiver
  ZF receiver :
LMMSE receiver

## Slide 69: Characterization of Wireless Channel

## Slide 70: Wireless Channel Model
Wireless channel model
    – number of multi-path components/channels
    - Channel attenuation
    - delay
An important characteristic of a multi-path channel is the time delay spread it causes to the received signal
This delay spread equals the time delay between
  The arrival of the first received signal component (LOS or multi-path)
  Last received signal component associated with a single transmitted pulse
If the delay spread is
  Small compared to the inverse of the signal bandwidth, then there is little time spreading in the received signal
  Relatively large compared to the inverse of the signal bandwidth, then there is significant time spreading of the received signal which leads to substantial signal distortion
Maximum delay spread
    - Last multi-path component received
    - First multi-path component received

## Slide 71: Wireless Channel Model – Delay Spread
Another metric for the delay spread is RMS delay spread
Let
Mean delay (Weighted average of delays)
RMS Delay Spread -
Typical delay spread in outdoor distances – 2-3s
When does ISI occur?
  - ISI
On the other hand
  – No ISI

## Slide 72: ISI Channel Model
No ISI channel model
  depends only on
ISI channel model
  –
    - linear convolution
    – channel taps or taps of the channel filter or coefficients of channel filter – FIR – Finite Impulse Response
  depends on
Delay spread
  So, ISI occurs when the bandwidth is greater than 250 kHz – this bandwidth is known as Coherence bandwidth and is represented by of the channel
The relationship between and is - - channel delay spread
Hence ISI occurs if:
So, - coherence bandwidth is inversely proportional to delay spread

## Slide 73: Delay Spread
Say delay spread
  Channel model
  Fourier transform
  BW=
Frequency domain interpretation of
  When signal bandwidth , the output spectrum is undistorted
    Channel response is flat over signal bandwidth
    Such a channel is termed as flat fading channel
    No ISI and no distortion
  When signal bandwidth
    Fading is frequency selective
    Channel response is NOT flat and varies over signal bandwidth
    Signal spectrum is distorted frequency domain and is ISI in time domain

## Slide 74: Doppler Shift
What happens when a mobile moves away or towards base station/transmitter
  Angle and velocity
  Change in the observed/received frequency by the receiver
  This is termed as doppler shift
Doppler shift
  – velocity of the mobile
  – speed of light
  - carrier frequency
  – angle between velocity vector and line joining mobile to base station
Impact of doppler shift on the channel
  Time varying delay Time Varying Channel
  Such a channel is called Time Selective Channel
How fast is channel varying?
  Let denote the time over which channel is constant
  This is termed Coherence Time
Higher velocity => coherence time is small
Doppler bandwidth =